## Slide 1: Distance Vector Routing Protocols
Dr. Rocky K. C. Chang 15 November 2010

## Slide 2: The routing problem
Problem: How can a router/host determine the path to a destination?
Any routing protocol must allow routers to make a corporate, consistent, and correct local forwarding decisions regarding any destination in a global routing fabric.
  Sources and destinations are generally not directly connected.
  Routers are generally not directly connected.

## Slide 3: Design issues
Scalability: scale to the number of networks
  Routing table size
  Routing messages
  Time to converge
Free of permanent/transient routing loops
Optimal paths: hop count, type-of-service, quality-of-service, etc.
Security
Host mobility and perhaps router mobility

## Slide 4: Design choices
Centralized vs decentralized
  A central processor computes the routes.
Source-based vs hop-by-hop
  E.g., source routing and destination-based routing
With or without the global topological info.
  E.g., OSPF vs RIP
Dynamic (or state-dependent) vs static routing
  IP routing vs ATM routing
Single-path vs multiple path

## Slide 5: Two main routing approaches
Distance vector (DV) and link state (LS)
  Both are implemented as distributed protocols.
  Both are hop-by-hop routing protocols.
  DV routers do not have the complete topological info but LS routers do (partially).
  Both are dynamic routing protocols.
  Both could maintain multiple paths.
Each DV router tells its neighbor routers what it has learnt. Each LS router tells all routers the states of its directly connected links.

## Slide 6: Distance vector approach
The origin of distance vector protocols is traced back to the Bellman-Ford algorithm. Let
  dij: the cost of the link from node i to node j, which is  if the link does not exist.
  Dij(h): the cost of the minimum-cost route from node i to node j on the number of h hops.
  Initial conditions:
  Dii(h) = 0 for all i and h, and Dij(0) =  for i  j.
  Iterative steps:
  Dij(h+1) = mink[dik + Dkj(h)] for all i  j.
  until Dij(h+1) = Dij(h) for all i and j.

## Slide 7: Bellman-Ford algorithm
Conditions:
  The link costs are additive.
  If all cycles not containing the destination have nonnegative length.
The Bellman-Ford algorithm
  terminates after a finite number of iterations (at most N, the number of nodes),
  gives minimum-cost paths from all nodes to other nodes, and
  its computational complexity in the worse case is O(N3).

## Slide 8: An example
A
B
E
C
D
7
1
1
2
2
8
A
B
E
C
D
7
1
A
B
E
C
D
7
1
1
2
A
B
E
C
D
7
1
2
2

## Slide 9: An example
1
A
B
E
C
D
1
2
2

## Slide 10: Distributed, asynchronous B-F algorithm
Node i executes the B-F algorithm asynchronously:
  Dii(t) = 0, for all i and t  0.
  Dij(t) = mink[dik + Dikj(t)] for i  j, where
  Dij(t) is the estimate of the cost to node j available to node i at time t.
  Dikj(t) is node k’s estimate of the cost to node j available to node i at time t.
Node i distributes its distance vector Dij(t) for all j to its neighbors.

## Slide 11: Distributed, asynchronous B-F algorithm
Node i also keeps the distance vectors sent from its neighbors.
The algorithm still converges if each node will eventually execute the algorithm and transmit the results to the neighbors.
  The convergence time, of course, depends on how quickly each node computes and distributes the results.
When the algorithm converges and there are no changes in the network, the transmissions of distance vectors stop.

## Slide 12: An example (from [1])
Consider that E-->A via D
Consider that E-->A via B
A
B
E
C
D
7
1
1
2
2
Dest
8

## Slide 13: Good news travels fast (from [1])
Consider
X
Y
Z
4
50
1
1

## Slide 14: Bad news travels slow (from [1])
Consider
X
Y
Z
4
50
1
60

## Slide 15: Bad news travels slow
When does the temporary routing loop stop?
  Count to infinity problem
Consider
X
Y
Z
4
1
fail

## Slide 16: Split horizon
If Z routes through Y to reach X, then Z will
  not advertise the route to X back to Y or
  advertise the router to X with infinite cost to Y (with poisonous reverse).
X
Y
Z
4
50
1
60

## Slide 17: Split horizon
In either case, Y is asked not to use Z as a next-hop to reach X.
In the last example,

## Slide 18: Split horizon
Split horizon can break temporary/permanent routing loops of 2 nodes but not for more than 2 nodes.
A certain “large” cost should be selected to represent the unavailability of a link.
X
Y
Z
4
1
fail
X
Y
Z
1
1
fail
4
1
W

## Slide 19: Path vector
Augment each distance vector entry with a path vector.
  Y advertises to Z about a route to X with a cost of 4 plus a path vector {Y}.
  Z advertises to Y about a route to X with a cost of 5 plus a path vector {Y, Z}.
  When Y receives the route, it checks whether its identity is in the path vector.
X
Y
Z
4
50
1

## Slide 20: Source tracing
Augment each distance vector entry with the identity of the router immediately preceding the destination, e.g., E-->B
  Trace the route to be B<--C<--D<--E.
A
B
E
C
D
7
1
1
2
2
8

## Slide 21: Distributed update algorithm (DUAL)
Each router keeps distance vectors reported by its neighbors.
If receiving a route that is better than the current one, use it.
  This new route is impossibly involved in a routing loop.
If the cost of the existing route increases, try to find a shorter route from the distance vectors.
  If not, freeze the routing table and propagate this change until all routers have updated them.

## Slide 22: Routing Information Protocol (RIP)
RIP is an implementation of the distance vector approach at the application level.
  Common daemons used on the Unix systems are the programs routed and gated.
  RIP packets are carried over UDP and IP.
Most RIP implementations use hop count (the number of routers traversed) as the cost.
  A hop count of 16 is interpreted as infinity.
Each node is a RIP router, which is generally connected to a number of networks.

## Slide 23: RIP-1 messages

## Slide 24: More protocol details
RIP routers only retain the current minimum-cost route and the corresponding next-hop routers’ identities.
  They do not keep the distance vectors from their neighbor routers.
  This form of implementation also inherits the same temporary/permanent routing loop problems, e.g., Y may receive an out-dated distance vector from Z before Y can send an updated one to Z.

## Slide 25: Triggered and periodic updates
To cater for link and router failures, each route will time out unless receiving a corresponding distance vector.
  Each RIP router broadcasts its distance vectors to its neighbors every 30 seconds (periodic updates).
  Timeout period may be set to 30x6 seconds.
To accelerate convergence, triggered updates are also employed.
  Immediately send cost updates to neighbor routers instead of waiting for periodic updates.
  Can avoid many routing loop problems.

## Slide 26: Hold-down
When a router removes a route, it invokes a hold-down that would not accept new routes to the same destination for a time period.
  During this period, the removed route is advertised to other routers (triggered update).
  The purpose is to allow the triggered update to propagate to other routers.
  Routing loops can be avoided if the time period is long enough.
The downside is to take longer for routers to learn new routes.

## Slide 27: RIP-2
RIP-2 improves RIP-1 by providing
  Subnet masks which facilitate subnet routing, CIDR, and variable length subnet masks
  Data authentication: a security leader and a security trailer (RFC 2082)
  Next hop: Allow packets destined to the IP address specified in RIP-2 messages sent to somewhere else (specified in the next hop field).
  multicasting of routing advertisements (224.0.0.9), instead of broadcasting

## Slide 28: RIP-2 messages
The route tag is used to flag “external routes,” and is used in conjunction with BGP.

## Slide 29: Conclusions
Internet routing is the “intelligence” of the network layer.
Distance vector routing has been deployed in the intra-domain routing protocols today.
However, it suffers from the slow convergence problem and it is prone to routing loops.
A number of additional mechanisms were added to the basic distance-vector routing, e.g., path vector, etc.

## Slide 30: References
J. Kurose and K. Ross, Computer Networking: A Top-Down Approach Featuring the Internet, Addison Wesley, 2001.
M. Steenstrup, Routing in Communications Networks, Prentice Hall, 1995.
S. Keshav, An Engineering Approach to Computer Networking, Addison Wesley, 1997.
C. Huitema, Routing in the Internet, Prentice Hall PTR, Second Edition, 1999.