## Slide 1: IP over anything
Dr. Rocky K. C. Chang 20 September 2010

## Slide 2: IP service model
The IP service model consists of
  an addressing scheme to identify a network interface, and
  a datagram (connectionless) model of data delivery.
R1
ETH
FDDI
IP
IP
ETH
R2
FDDI
ETH
IP
H1
IP
ETH
H2
IP
IP
IP

## Slide 3: IP service model
IP provides an unreliable and connectionless (datagram) delivery service, which is often referred to as a best-effort service.
  Connectionless (vs connection-oriented):
    The IP network processes each IP packet independently.
    Destination based packet forwarding
  Unreliability (vs reliable IP): do not ensure that
    the packets will be delivered to the destination.
    the packets will be delivered to the destination correctly.

## Slide 4: IP service model
    the packets will be delivered in the same order as they were sent.
    the packets will not be duplicated.
Best-effort service was the result of design instead of default.
  Reliability is an additional service, provided by the transport layer.
  What need to be done to the IP layer if total reliability is required there?

## Slide 5: IP over anything?
IP over LANs and MANs
IP over WANs
IP over ATM
IP over fiber
IP over wireless networks
IP over Bluetooth
IP over satellite
IP over powerline
IP over space

## Slide 6: Assumptions made by IP
IP made a minimal set of assumptions about the function of that the network to be connected would provide.
  The network can transport a packet, which must be of reasonable size.
  The packets should be delivered with reasonable reliability but not perfect reliability.
  The network must have some suitable form of addressing if it is more than a point-to-point link.

## Slide 7: Requirements for using IP
To transmit IP datagrams over any networks, two requirements need to be fulfilled:
  Have a standard way to frame or encapsulate an IP datagram.
  Have a method of resolving an IP address to the MAC address of the underlying network.

## Slide 8: IP over legacy LANs
IP over Ethernet (RFC 894), IEEE 802 (RFC 1042), FDDI (RFC 1188), etc.
Ethernet frames:
CRC
Dest address
Src address
Type
Data
Type 0800
IP datagram
Type 0806
ARP request
Type 8035
ARP reply

## Slide 9: IPv4 addresses
A, B, C, D classes of addresses (classful addresses)
Network
Host
7
24
0
Network
Host
14
16
1
0
Network
Host
21
8
1
1
0
28
1
1
0
1
Class A
Class B
Class C
Class D

## Slide 10: IP subnets
IP subnets introduce additional levels within an IP network:
  A network address, a subnet ID, and a host ID.
IP subnets offer flexibility in allocating addresses to different sizes of sub-networks.
A subnet mask is used to indicate which bits are referred to the network and subnet ID.
  Each network interface stores subnet mask and its unicast IP address.

## Slide 11: IP subnets
Subnetting for a class B address (/24)
Variable-length subnet mask
Network number
Host number
Class B address
Subnet mask (255.255.255.0)
Subnetted address
111111111111111111111111
00000000
Network number
Host ID
Subnet ID

## Slide 12: IPv4 address assignment
R2
R1
H4
H5
H3
H2
H1
Network 2 (Ethernet)
Network 1 (Ethernet)
H6
Network 3 (FDDI)
Network 4
(point-to-point)
H7
R3
H8

## Slide 13: IP supernets
Have a subnet mask shorter than the network address.
For example, use a “subnet mask” of 255.255.252.0 (/22) for
  Network 222.231.32.0
  Network 222.231.33.0
  Network 222.231.34.0
  Network 222.231.35.0
Purpose of doing this?

## Slide 14: IP broadcast addresses
Broadcast addresses
  Net ID = all 1s and host ID = all 1s (limited broadcast)
  Net ID != all 1s and host ID = all 1s (network-directed broadcast)
  IP broadcast vs data-link broadcast
Multicast addresses
  224.0.0.0/4
  Reserved multicast addresses (e.g., 24.0.0.1 for all systems on this subnet)

## Slide 15: IPv4 special unicast addresses
Special source addresses: NetID = 0.0.0.0/8
Loopback addresses: 127.0.0.0/8
Link-local addresses: 169.254.1.0/16
Three classes of private addresses: 10.0.0.0/8, 172.16.0.0/12 and 192.168.0.0/16
6-to-4 anycast addresses: 192.88.99.0/24 (RFC 3068)
Reserved for special use and for future allocation

## Slide 16: Private IPv4 addresses
To reduce the required number of IP addresses, three blocks of IP address space are reserved for private internets (RFC1918):
  10.0.0.0/8
  172.16.0.0/12 (16 class B networks)
  192.168.0.0/16 (256 class C networks)
Private addresses are also known as nonroutable addresses

## Slide 17: Private IPv4 addresses
A host with a private IP address may communicate with external hosts through a Network Address Translation (NAT) service.
  Address and port translations
  NAT is usually provided by a firewall or a border router.
  The private address is translated into a nonprivate IP address before sending the datagram out.

## Slide 18: Address configuration
Static vs auto configurations
Stateful vs stateless configurations
  Stateful: DHCP
  Stateless: Link local addresses (169.254.0.0/16)
    Communication within a single link
    Link-local addresses are also not routable.
    Zero configuration networking

## Slide 19: Address resolution in shared media
Two approaches: server-based or broadcast-based
In the broadcast-based approach:
  An (address resolution protocol) ARP request message is data-link broadcast on the LAN with the target IP address.
  Every IP host picks up a copy of the message and examines the target IP address.
    If matching its IP address, send an ARP reply message back to the sender with its MAC address.
    Else, drop the message.

## Slide 20: ARP frames for Ethernet
T
argetHardwareAddr (bytes 2
–
5)
T
argetProtocolAddr (bytes 0
–
3)
SourceProtocolAddr (bytes 2
–
3)
Hardware type = 1
ProtocolT
ype = 0x0800
SourceHardwareAddr (bytes 4
–
5)
T
argetHardwareAddr (bytes 0
–
1)
SourceProtocolAddr (bytes 0
–
1)
HLen = 48
PLen = 32
Operation
SourceHardwareAddr (bytes 0
–
3)
0
8
16
31

## Slide 21: Other enhancements and usage
To reduce broadcast traffic, each host uses an ARP cache to remember the recent binding.
Gratuitous ARP
  A host sends out an ARP request message at bootstrap, looking for its IP address.
  The sender’s protocol address and the target’s protocol address are identical.
  Purposes?

## Slide 22: Other enhancements and usage
Proxy ARP
  Map a single MAC address onto multiple IP addresses.
  A router, configured with proxy ARP, answers ARP requests on behalf of the target host.
  The router also needs to build up a database on (MAC address, IP address) for all hosts attached to the router.
The broadcast approach has one potential problem---broadcast storm.
Reverse ARP (RARP)

## Slide 23: Additional internetworking issues

## Slide 24: Additional internetworking issues
Bridging heterogeneous MTU
Handling packet reordering
Error detection and reporting
Providing “differentiated” services
Packet scoping
Providing other forms of routing
Network diagnosis

## Slide 25: Heterogeneous MTUs
Each network chooses a maximum packet size that can be sent on it, Maximum Transmission Unit (MTU). For example,
  1500 bytes for 10-Mbps Ethernet
  4352 bytes for FDDI
  17914 bytes for 16-Mbps token ring
  9180 bytes for ATM AAL5
  9000 bytes for Ethernet jumbo frames
Over-sized frames will be dropped.
All MTUs are smaller than IP datagram’s maximum size (65,535 bytes)

## Slide 26: Heterogeneous MTUs
If MTU1 > MTU2
Minimum MTU = 576 bytes (RFCs 791 and 879)
R
MTU1
MTU2

## Slide 27: Path MTU
Path MTU: The minimum of the networks’ MTUs on the path from the source to destination.
Path MTU between H1 and H2 = min{MTU(N1), MTU(N2), MTU(N3)}
How to find the path MTU?
N1
N2
N3
H1
H2

## Slide 28: Approaches to bridging MTUs
Problem: How can an IP datagram traverse networks with different MTUs?
  Recall that IP does not assume that all MTUs are the same.
Approaches
  Always use the minimum MTU.
  Use the local MTU first and then use the minimum MTU if it is not successful.
  Network-centric
  Host-centric

## Slide 29: Hop-by-hop IP fragmentation: A network-centric approach
Transparent to the sending host
A router fragments an IP packet when forwarding it to a network with a smaller MTU.
Each IP fragment contains enough information for forwarding to the destination.
  Remember the connectionless model?
A fragmented IP datagram will be reassembled only at the destination node.
  Why not reassembled at intermediate routers?

## Slide 30: Fragmentation considered harmful?
Fragmentation causes inefficient resource usage (bandwidth, computation)
Loss of fragments leads to degraded performance.
Efficient reassembly is hard.

## Slide 31: Fragmentation considered harmful?
A recent report on the characteristics of fragmented IP packets
  Fragmented traffic does regularly occur at highly aggregated exchange points as well as on access links.
  Majority of fragmented traffic is UDP (68% by packets and 72% by bytes)
  ICMP, IPSec, TCP, and tunneled traffic are all present.
  Tunneled traffic forms a large portion of fragmented traffic (16% by packets and 11% by bytes)

## Slide 32: Packet reordering
According to a recent study, packet reordering is a common phenomenon in the Internet today.
Packet reordering is strongly a function of the following properties of the routing path.
  Parallel links between nodes on the path
  Exact configuration of the hardware and software in the nodes
  The load on the nodes.
Impact of reordering on TCP performance

## Slide 33: Packet reordering
B6
B4
B3
B1
B5
C2
B2
C1
D1
C2
C1
C2
C1
A1 A2 B C D
A1 A2 B C D

## Slide 35: What can IP do to packet reordering?
Make IP aware of the parallel links and direct which link each packet flow is sent over.
  Hash the source and destination IP addresses modulo the number of links
A number of pitfalls:
  A single flow cannot use all the parallel links
  Uneven distribution of the flows on the links

## Slide 36: Summary
By design, IP provides the best-effort service to deliver IP datagrams on top of various networks.
Besides address resolution and packet encapsulation, IP also needs to handle the heterogeneous MTU issue and others.
The IP datagram was carefully designed (not) to address other issues.

## Slide 37: References
J. Bennett, C. Partridge, and N. Shectman, “Packet Reordering is Not Pathological Network Behavior,” IEEE Trans. Networking, vol. 7, no. 6, pp. 789-798, 1999.
C. Shannon, D. Moore, and k claffy, “Characteristics of Fragmented IP Traffic on Internet Links,” available from http://www.caida.org/outreach/papers/2001/Frag/
C. Kent and J. Mogul, “Fragmentation Considered Harmful,” ACM Computer Commun. Rev., pp. 75-87, Jan. 1995.