## Slide 1: Basics of Wireless Communications
Analog vs. Digital transmission
Frequency, Spectrum, Bandwidth
Modulation Techniques
Multiplexing Techniques
Medium Access Control (MAC)
Notes: Application developers do not have to know the internal working of wireless networks to be successful, but having knowledge of how they work is very helpful.
Understand why certain wireless technologies behave the way they do;
Understand which application design architectures should be based.

## Slide 2: Networking Layers
Notes: Application developers do not have to know the internal working of wireless networks to be successful, but having knowledge of how they work is very helpful.
Understand why certain wireless technologies behave the way they do;
Understand which application design architectures should be based.

## Slide 3: Analog vs. digital data
Data can be digital or analog
  Digital data appears as a sequence of bits, each of it taking on one of two discrete values: the binary 0 and the binary 1.
    e.g., text
  Analog data is characterized by a continuous value range at some interval.
    e.g., human speech.

## Slide 4: Analog vs. digital signal
Signals can also be digital or analog:
  Digital signal - signal strength (voltage pulses) maintains a constant level for some period of time and then changes to another constant level
  Analog signal - signal strength varies in a smooth (continuously varying) fashion over time

## Slide 5: Analog vs. digital signal
Both analog and digital data can be propagated by analog and digital signals

## Slide 6: Analog vs. digital signal
Digital signal
  generally cheaper than analog signaling
  less susceptible to noise interference
  allow better utilization of the bandwidth
  suffer more from attenuation, which endangers integrity of data
    repeaters can be used to recover the signal and retransmit for longer distance (in wired networks)

## Slide 7: Frequency
An electromagnetic wave is characterized by:
  Amplitude (A) - maximum strength of the signal over time; typically measured in volts
  Frequency (f ) - rate at which the signal repeats, measured by cycles per second (called Hertz (Hz))
  Phase () - denotes the relative position in time within a single cycle of a signal
  Wavelength () - distance occupied by a single cycle of the signal - the distance between two points of corresponding phase of two consecutive cycles

## Slide 8: Frequency
The higher the frequency, the shorter the wavelength.
  In vacuum, all electromagnetic waves transmit at the same constant speed C (speed of light: C  3x108m/s), independent of their frequencies: C = f
The higher the frequency, the higher the bit rate.
  More changes can be expressed
  e.g., under low frequency, only several bits can be encoded, but under high frequency, sometimes can encode up to 40 bits.
The higher the frequency, the smaller the components become (e.g., antennas)
  Today’s cellular phone are so small because they operate at frequencies high enough to allow components inside to be made small enough

## Slide 9: Modulation
An electromagnetic wave does not carry any information in its pure form. In order to represent data, one or more of its parameters A, f, and  need to be varied over time.
  This is called modulation: signals are manipulated to carry information, or data is superimposed onto the carrier signal
Conventional standard modulation methods are:
  Amplitude modulation – varying A,
  Frequency modulation – varying f,
  Phase modulation – varying 

## Slide 10: Modulation

## Slide 11: Spectrum, Bandwidth
The original carrier signal consists of only a single frequency but, when modulating data onto it, the modulated carrier signal can be spread over a range of several frequencies.
Spectrum - range of frequencies adopted by a modulated carrier signal [fmin, fmax].
Bandwidth - width of the spectrum, or the difference between the highest and lowest frequencies available in a band (fmin- fmax)

## Slide 12: Channel capacity
The following two terms have benn used interchangeably for describing the information transmission capability of a network.
Bandwidth : range of signal frequencies that can be supported
  Used in analog networks - unit is Hz, KHz, MHz and GHz
  e.g. telephone lines carrying analog signals have a bandwidth from 300 Hz to 3.4 KHz
Data rate : number of bits that be transmitted in a unit of time
  Used in digital networks - unit is bps, Kbps, Mbps, and Gbps
  e.g. digital voice signal passes at a speed of 64Kbps; optical fiber can carry digital signals at a speed of 20 Gbps.

## Slide 13: Channel capacity
The greater the bandwidth, the higher the information-carrying capacity (transmission rate, or data rate)
Any digital waveform has infinite bandwidth, but it is the transmission system that limits the bandwidth that can be transmitted
  For any given medium, the greater the bandwidth transmitted, the greater the cost
  On the other hand, limiting the bandwidth creates distortions

## Slide 14: Channel capacity
Narrowband (or Voiceband)
  Used for regular telephone communications
  Transmission rate < 100 kilobits per second
Mediumband
  Used for long-distance data transmission or to connect mainframe and midrange computers
  Transmission rate 100 kb to 1 megabit per second
Broadband
  For high-speed data and high-quality audio and video
  Transmission rate 1 megabit per second to 100 megabits per second

## Slide 15: Electromagnetic spectrum
Wireless networks may use different bands in the electromagnetic spectrum
  Each band consists of a range of frequencies
  Majority of wireless networks use the bands of radio waves and microwaves
  Some use Infrared (e.g., for household devices)
  The spectrum is a continuum; the boundaries between different bands don’t exist naturally, but were invented by scientists trying to classify them

## Slide 16: Electromagnetic spectrum
Signals for wireless communications are classified into radio, microwave, infrared

## Slide 17: Electromagnetic spectrum

## Slide 18: Frequency bands for wireless communications
Radio frequency range
  30 MHz to 1 GHz
  Suitable for omnidirectional applications
Microwave frequency range
  1 GHz to 40 GHz
  Higher-frequency bands are suitable for point-to-point transmission
  Used for satellite / radar communications
  Also used for heating
Infrared frequency range
  Roughly, 3x1011 to 2x1014 Hz
  Useful in local point-to-point / multipoint applications within confined areas
  Remote control, optical networks
These bands are relevant to telecommunications (ELF – EHF) and fixed by ITU – Int’l Telecom Union.

## Slide 19: Modulation in wireless networks
Special transmission techniques are used in wireless communications.
  e.g., WLANs, mobile phone networks, digital radio system DAB (Digital Audio Broadcast), etc.
  Unlike in narrowband technology (data is transmitted on designated carrier frequency), here multiple frequencies are used.
Different techniques are available, differing in efficiency, power requirements, and complexity.
  Spread spectrum
  Orthogonal Frequency Division Multiplexing (OFDM)
Notes: Why do we need new techniques?
For saving precious bandwidth by improving bandwidth utilization
For reducing interferences

## Slide 20: Spread spectrum
Distribute a signal over a wide range of frequencies for transmission
Two variations exist:
  DSSS (Direct Sequence Spread Spectrum)
  FHSS (Frequency Hopping Spread Spectrum)

## Slide 21: DSSS
Each bit in original signal is represented by multiple bits in the transmitted signal
  Spreading code is used to mix with each message bit before it is transmitted – the effect is spreading the signal across a wider frequency band.
    Spread is in direct proportion to number of bits used
  The same code is used to decode these encoded bits.
One technique combines digital data stream with the spreading code bit stream using exclusive-OR

## Slide 22: DSSS
user data
Code bit
sequence
resulting
signal
XOR
=
0 1

## Slide 23: FHSS
Signal is broadcast over seemingly random series of radio frequencies
  A number of channels are allocated for the FH signal
  Width of each channel corresponds to bandwidth of input signal
  Signal hops from frequency to frequency at fixed intervals
Transmitter operates in one channel at a time
  Bits are transmitted using some encoding scheme
  At each successive interval, a new carrier frequency is selected
Receiver, hopping between frequencies in synchronization with transmitter, picks up message

## Slide 24: FHSS

## Slide 25: FHSS
user data
slow
hopping
(3 bits/hop)
fast
hopping
(3 hops/bit)
0
1
tb
0
1
1
t
f
f1
f2
f3
t
td
f
f1
f2
f3
t
td
tb: bit period td: dwell time

## Slide 26: Features of spread spectrum
Allow multiple users to use the same frequency band
  Easily detected by receivers that know the parameters (patterns) of the signal being broadcast.
  To everyone else the spread-spectrum signal looks like background noise
Higher reliability and security
Used in most mobile data transmission systems, including Bluetooth, 3G cellular networks, and WLAN

## Slide 27: Multiplexing
Multiplexing - carrying multiple users’ signals over a single medium
  Capacity of transmission medium usually exceeds capacity required for transmission of a single user – how to make more efficient use of transmission medium
  The medium is always shared in wireless communication – how to ensure low interference.
  Divide medium into several channels that can be used independently of each other without interferences.

## Slide 28: Multiplexing techniques
Frequency-division multiplexing (FDM)
  Takes advantage of the fact that the useful bandwidth of the medium exceeds the required bandwidth of a given signal
  Advantages:
    no dynamic coordination necessary
    works also for analog signals
  Disadvantages:
    waste of bandwidth if the traffic is distributed unevenly
    inflexible

## Slide 29: Multiplexing techniques
Time-division multiplexing (TDM)
  Takes advantage of the fact that the achievable bit rate of the medium exceeds the required data rate of a digital signal
  Advantages:
    only one carrier in the medium at any time
    high throughput even for many users
  Disadvantages:
    Precise coordination and synchronization necessary

## Slide 30: Multiplexing techniques
Code-division multiplexing (CDM)
  Takes advantage of the fact that multiple channels can take place using the same frequency at the same time, if we separate the channels by assigning them their own ‘code’
  Implemented using spread spectrum technology - DSSS
  Advantages:
    Bandwidth efficient
    Good protection against interference and tapping
  Disadvantages:
    More complex signal regeneration
    Precise power control needed

## Slide 31: CDM examples
Sender A
  sends Ad = 1, Code Ac = 010011 (Let “0“= -1, “1“= +1, Ak = -1 +1 -1 -1 +1 +1)
  sending signal As = Ad * Ak = (+1) * (-1, +1, -1, -1, +1, +1)
  = (-1, +1, -1, -1, +1, +1)
Sender B
  sends Bd = 0, Code Bc = 110101 (Let “0“= -1, “1“= +1, Bk = +1 +1 -1 +1 -1 +1)
  sending signal Bs = Bd * Bk = (-1) * (+1, +1, -1, +1, -1, +1)
  = (-1, -1, +1, -1, +1, -1)
Both signals superimpose in space
  interference neglected (noise etc.)
  As + Bs = (-2, 0, 0, -2, +2, 0)
Receiver wants to receive signal from sender A
  apply code Ac bitwise (inner product)
    Ae = (-2, 0, 0, -2, +2, 0)  Ak = 2 + 0 + 0 + 2 + 2 + 0 = 6
    result greater than 0, therefore, original bit was “1“
  receiving B
    Be = (-2, 0, 0, -2, +2, 0)  Bk = -2 + 0 + 0 - 2 - 2 + 0 = -6, i.e. “0“

## Slide 32: CDM examples

## Slide 33: Multiplexing techniques
Space-division multiplexing (SDM)
  Allow the establishment of several channels in the same frequency range for simultaneous use, assuming that they are sufficiently separated in space.
  Define frequency reuse distance (e.g., Cell structure, where signals are attenuated as farther away they travel from the source). or
  Propagate signals as highly directed beams (e.g., Segment space into sectors, use directed antennas)

## Slide 34: OFDM
Transmits data over parallel frequencies
  A special method of implementing MCM (multi-carrier modulation)
    Channel bandwidth is divided into multiple sub-carrier frequencies called tones (sub-channels)
    Fast serial data stream is converted into slow parallel streams (longer symbol durations), and then distributed over different sub-carriers for transmission.

## Slide 35
Channel impulse
response
1 Channel (serial)
Channel
transfer function
Channels are
“narrowband”
2 Channels
Frequency
Frequency
8 Channels
Frequency
Frequency
Time
Signal is
“broadband”

## Slide 36: OFDM
Same as in traditional FDM, sub-carriers are spaced apart, but in OFDM they can be overlapped to be independent & unrelated, hence orthogonal.
Spectrum of normal time
domain sequence
Spectrum of classical
FDM
Spectrum of OFDM

## Slide 37
Ch.1
Ch.2
Ch.3
Ch.4
Ch.5
Ch.6
Ch.7
Ch.8
Ch.9
Ch.10
Saving of bandwidth
Ch.3
Ch.5
Ch.7
Ch.9
Ch.2
Ch.4
Ch.6
Ch.8
Ch.10
Ch.1
Conventional multicarrier techniques
Orthogonal multicarrier techniques
50% bandwidth saving
frequency
frequency

## Slide 38: OFDM
Used by IEEE 802.11a/g & 802.16
Advantages:
  Protecting signal from interference
  High spectrum efficiency – more data can travel over a smaller amount of bandwidth

## Slide 39: Multiple access methods
Multiplexing is about how to share the medium by dividing the medium into multiple channels
But how to use multiplexing ?
This is by multiple access methods :
  Segmenting available spectrum into frequencies,
  planning frequency for reuse,
  allocating time slots, or
  defining spreading codes, etc..

## Slide 40: Multiple access methods
FDMA (Frequency Division Multiple Access)
  Based on FDM – Allocate frequencies to channels or define a frequency hopping pattern
  E.g., used for simultaneous communication between base station and mobile unit (uplink and downlink)
TDMA (Time Division Multiple Access)
  Based on TDM – Allocate time slots for channels in a fixed pattern;
CDMA (Code Division Multiple Access)
  Based on CDM – Assign codes to allow for separation of different users in code space;
  Power control (the problem of “near and far terminals”).
SDMA (Space Division Multiple Access)
  Based on SDM

## Slide 41: Multiple access methods

## Slide 42: Comparison of FDMA, TDMA, CDMA (example: Cellular system)
f4
f5
f1
f3
f2
f6
f7
f3
f2
f4
f5
f1

## Slide 43: Call Admission Control
Given the number of channels available, the network needs to determine whether a newly arrived transmission request should be admitted.
This is especially important for calls in cellular phone networks - the Call Admission Control (CAC) problem
  The number of channels allocated to each BS is limited
  Maximized channel utilization while guaranteeing QoS

## Slide 44: Call Admission Control
CAC is a process for managing the arriving traffic (at the call, session, or connection level) based on some predefined criteria
When necessary, some call requests need to be blocked
  New call blocking
  Handoff call blocking
Example: TDMA network

## Slide 45
At instant (t2), one of the 17
active users in cell 2 is leaving cell 2
heading cell 3.
This user has to be handed over
to cell 3, but cell 3 is fully loaded.
Result: This user will be rejected
by cell 3 and the call will be dropped.
Conclusion:
Admitting the new user in cell 2 at
instant (t1) was not a good decision.
Number of channels per cell=20.
The network consists of 3 cells.
At instant (t0), number of users Ni(t0) (i=1,2,3) is equal to (18, 17, 19)
At instant (t1), a new user arrived at cell 3. Then Ni(t2) will be (18, 17,20).
The Guard Channel Scheme
  Parameter to consider: new and handoff call arrival rates and mean call residency time

## Slide 46: Call Admission Control
Naïve solution: for no hand-off drops, reserve bandwidth in all cells a mobile/connection might pass through
Problem: bandwidth quickly consumed and new connection blocking probability increases
Proposed solution: a cell estimates aggregate bandwidth for hand-offs from adjacent cells, to be reserved and used solely for hand-offs, not new connection requests
  Predictive: estimate directions and hand-off times of ongoing connections in each cell
  Adaptive: dynamically adjust amount of reserved bandwidth to account for estimation inaccuracies and varying traffic/mobility conditions

## Slide 47: Medium Access Control (MAC)
Multiplexing allows terminals to share medium, assuming each terminal can be assigned a separate channel in the medium for transmission (e.g. by CAC).
But in some networks, channels are accessed by terminals on demand - there is no admission control and no dedicated channel for each terminal. Then terminals need to compete for the use of channels and collision may occur.
MAC protocols are used to regulate multiple terminals for randomly access to the shared medium.
  Need to resolve collisions - can be centralized and distributed
  Needed for wireless networks that are designed to carry data: IEEE 802.11 Wireless LANs, ad hoc networks, bluetooth, ….

## Slide 48: Medium Access Control (MAC)
MAC in wireless networks is more difficult than in wired network
  Signal strength decreases proportional to square of distance, so no use for sender to apply CS
  Collisions happen at receivers, so no use for sender to apply CD
Protocols (centralized vs distributed; schedule-based vs. conflict-based)
  ALOHA,
  CSMA/CA (Carrier Sense MA with Collision Avoidance),
  MACA (MA with Collision Avoidance),
  DAMA (Demand Assignment MA – for Satellites),
  …

## Slide 49: Medium Access Control (MAC)
Hidden terminal problem
  A sends to B, C cannot receive A
  C wants to send to B, C senses a “free” medium (CS fails)
  Collision at B, A cannot receive the collision (CD fails)
  A is “hidden” for C -> cause collisions

## Slide 50: Medium Access Control (MAC)
Exposed terminal problem
  B sends to A, C wants to send to D
  C has to wait, CS signals a medium in use
  Since A is outside radio range of C, waiting is not necessary
  C is “exposed” to B –> unnecessary blocking

## Slide 51: Medium Access Control (MAC)
Near and far terminal problem
  The signal of terminal B hides A’s signal
  C cannot receive A as B can keep occupying the channel
  This is also a severe problem for CDMA networks - precise power control is needed

## Slide 52: Medium Access Control (MAC)
Example: MACA (Multiple Access with Collision Avoidance)
  Use short signaling packets for collision avoidance;
  Request (or Ready) to send (RTS): sender requests the right to send from a receiver with a short RTS packet before it sends a data packet;
  Clear to send (CTS): receiver grants the right to send as soon as it is ready to receive
  Signaling packets contain:
    Sender address
    Receiver address
    Packet size

## Slide 53: Medium Access Control (MAC)
MACA avoids hidden terminal problem
  A and C want to send to B
  A sends RTS first
  C waits until receiving CTS from B
MACA avoids exposed terminal problem
  B wants to send to A and C wants to send to D
  Now C does not have to wait as it cannot receive CTS from A

## Slide 54: Research on MAC
Energy efficiency
Improving throughput (channel utilization)
Improving fairness
…