## Slide 1: Data Dissemination over Wireless Internet

## Slide 2: Wireless data dissemination
Application distribution service
  Information feeds:
    Stock quotes and sport tickets, electronic newsletters, mailing lists, traffic and weather information systems, cable TV on the Internet.
  Commercial products:
    AirMedia’s Live Internet broadcast network,
    Hughes Network Systems’ DirectPC

## Slide 3: Wireless data dissemination
Abstraction model
  Server
  Base station
  Clients
  Wireless channels
    Uplink channels for sending data query requests
    Downlink channel to receive data from BS

## Slide 4: Wireless data dissemination
Goals:
  Reduce access delay
    Wireless networks have less bandwidth and long delay
  Minimizing energy consumption at client
    MUs have limited energy power
  Maximize capacity of servers

## Slide 5: Wireless data dissemination
Two basic approaches for data dissemination
  Pull-based mechanisms (on-demand mode) - Client actively pulls data from the server
    music album server, ring tones server, video clips server, or bank account activity server
  Push-based mechanisms (publish-subscribe mode) - Server actively pushes data to client - as per the subscription for a push service by a client
    advertisers or generators of traffic congestion, weather reports, stock quotes, and news reports
Hybrid mechanisms (hybrid mode)

## Slide 6: Pull-based mechanisms
client
client
client
client
client
client
client
server
help

## Slide 7: Pull-based mechanisms
Pull is the best option when the server has very little contention and is able to respond to many device requests within expected time intervals
No unsolicited or irrelevant data arrives at the device
  Relevant data disseminated only when user asks for it

## Slide 8: Pulling bandwidth
Bandwidth used for the uplink channel depends upon the number of pull requests
  Assume uplink bandwidth of 19.2 kbps and server accepts 384 kbps, only 20 pull requests can be used at 19.2 kbps
  If number of pull requests is larger, uplink channel bandwidth lowered to 9.8 kbps or 4.8 kbps
  Similarly, server adapts to the bandwidth required for serving requests (downlink) in case the server is unable to deliver response in a reasonable period
Pull threshold limits the number of pull requests in a given period of time
  Controls the number of server interruptions

## Slide 9: Push-based mechanisms
client
client
client
client
client
client
server
Whew!

## Slide 10: Push-based mechanisms
Push is suitable when information is transmitted to a large number of clients with overlapping interests.
  The server saves several bandwidth and is prevented from being overwhelmed by client requests.
  Push is scalable: performance does not depend on the number of clients. Pull cannot scale beyond the capacity of the server or the network.
In push, access is sequential, so access latency degrades with the volume of data.

## Slide 11: Push algorithms
Select a structure of data records to be pushed
  an adaptable mechanism that permits data items to be pushed uniformly or non-uniformly after structuring them according to their relative importance
Push the data at selected time intervals
  pushing at periodic intervals provides the devices that were disconnected at the time of previous push with a chance to get the data when it is pushed again
Allocate bandwidths for downlink (for pushes)
  Usually higher bandwidth is allocated to data records with higher number of subscribers or higher access probabilities
Stop pushes when device is handed over to another BS

## Slide 12: Hybrid mechanisms
client
client
client
client
client
client
client
server
help
Whew!

## Slide 13: Hybrid mechanisms
Two channels between devices and server
  Front channel for push and Back channel for pull
  Bandwidth is shared and adapted between the two channels
    Bandwidth adapted in downlink and uplink channels depend upon the number of active devices receiving data from the server and the number of devices requesting data pulls from the server

## Slide 14: Wireless data broadcast

## Slide 15: Wireless data broadcast
Server continuously broadcast a set of most frequently accessed data on some fixed radio frequency channel.
  Mobile users receive broadcast data packets from the server by tuning their mobile units to this broadcast frequency, listen and download the desired data to local cache.
  Server determines, according to users’ demands or their interests, what data should be broadcast and its schedule on the channel.
A broadcast program consists of a set of data items, ordered in time of broadcast
  The program can also use index or some other method to inform users when their interested data are available, so as to save battery consumption on mobile units.

## Slide 16: Wireless data broadcast
service provider
Mobile users
Server
MU
MU
MU
.
.
.
Data
Distribution
Medium
A
A
A
A
A
A
A
B
B
B
B
Broadcast Program
optimized for expected
access pattern
of all users
individual access
pattern of one user


## Slide 17: Pure vs. On-demand broadcast
Pure broadcast
  MUs do not send any query but listen passively to the channel for interesting data items – e.g., stock quote
On-demand broadcast
  MUs send queries, and the result to a query is broadcast together with results from other queries on the same channel.
  MU must filter out the designated result.

## Slide 18: Models for wireless broadcast
1
2
3
4
5
6
server
Schedule of data blocks to be transmitted

## Slide 19: Models for wireless broadcast
Assume that records to be broadcast are stored on a hypothetical circular disk - the disk revolves and the angle changes from 0° to 360°
The entire N bits in n records get pushed through a hypothetical reading-head over the disk.
The head continuously reads each bit of a record just beneath it and broadcasts it instantaneously on the wireless network
During next revolution each bit in the records positioned from 0° to 360°broadcast once again in the same sequence as in earlier revolution
In case a device misses a record in first revolution, it can cache the same in next or any of the successive revolutions

## Slide 20: Models for wireless broadcast
Ts = time taken for one revolution of the disk
  Time interval between successive broadcasts of each bit in each record
  Ts = N × ts
ts = time interval between successive bits transmitted
  Time interval between transmission of successive bits
  ts = (Ts/N) [= reciprocal of bandwidth]
Due to sequential access of broadcast data items, increasing number of broadcast items causes mobile users to wait for longer time before receiving desired data items.

## Slide 21: Access Time
The main purpose of broadcast is to push records of greater interest with greater frequency in order to reduce access time or average access latency
taccess = the time interval between request from device and reception of interested data item from broadcasting or data pushing or responding system
  taccess is dependent on the number (n) and size (N) of the records to be broadcast
    the greater the n and N, the greater will be taccess

## Slide 22: Tuning Time
MU should be activated for listening and caching only when it is going to receive the elected data records or buckets of interest
  MU does not have sufficient energy to continuously cache the broadcast records and hoard them in memory
  MU dissipates more power if it gets each pushed item and caches it
Tuning means that MU gets ready for caching at those instants and intervals when a desired record of interest is broadcast
    ttune = time MU spent on listening actively to the channel
    Since MU must scan the channel for interested data item, its power consumption can be considered as directly proportional to ttune

## Slide 23: Access Time & Tuning Time
Do they have any correlation?

## Slide 24: Broadcast disks
Recall that broadcast-disk programs consists of a set of data items on the disk, ordered in time of broadcast.
Item-based broadcast program is expensive to generate, especially when there are many items
For better performance we can collect items of similar access probability into partitions.
  Each partition is viewed as an individual disk.
  Broadcast disks - Put items into different disks with different spinning speed.
  Broadcasting hot partitions more often translates into a disk spinning with faster speed.
  Multiplex multiple disks onto the same broadcast channel.

## Slide 25: Broadcast disk models
A broadcast file is similar to a disk file but located on the air – so it is also called broadcast disk - file on the air
Several disk models
  Flat Disk Model
  Circular Multi-disk Model
  Multi-disk Model with repetition rate proportional to priority
  Skewed disk model

## Slide 26: Broadcast disk models
Flat Disk Model
  Data records, R0, R1, R2, R3, R0, R1, R2, R3, are transmitted in a single broadcast cycle
  All record blocks have an equal priority level (round-robin)
  Server broadcasts the data as per cyclic requests (subscriptions) without taking into account the number of devices that subscribe to a particular record

## Slide 27
Circular Multi-disk Model
  Each block of records is pushed with a repetition rate proportional to its hierarchical level
Broadcast disk models

## Slide 28: Broadcast disk models
Multi-disk Model with repetition rate proportional to priority
  The transmission rate at each level is same but the repetition rate of a record is proportional to the record’s priority level
    Popular records are assigned to multiple levels.
    Priority of a record can be as per the number of users subscribing to it
3 priority levels

## Slide 29: Broadcast disk models
Skewed disk model
  Block of records are repeated as per their priorities for pushing
    Priority of a record can be set as per number of its subscribers
  Unlike the multi-disk model, the skewed-disk model entails consecutive repeated transmissions of a record block, followed by consecutive repeated transmissions of another record block, and so on

## Slide 30: Broadcast disk models
Skewed disk model
High priority record blocks pushed more often than the low priority ones because these are repeated one after one more often

## Slide 31: Objectives of broadcast disk program
Allow mobile users to access broadcast data with optimal access time and power consumption.
Determine how to organize the data items (e.g., in priority order) and schedule the time of broadcast (e.g., how often).
Determine how MUs should retrieve and process the broadcast data items on air.

## Slide 32: Broadcast disk program
Schedule of periodic broadcast of one or more disks
  Disks are of different sizes and can be broadcast at different speed
  Broadcast frequency of each item depends on its access pattern
B
C
A
Disk1
Disk2
A B A C

## Slide 33: Broadcast disk program
Disk parameters:
  first, the number of disks (i.e., different frequencies);
  then, for each disk, the number of data items to be stored and the relative frequency of broadcast
Scheduling Problem:
  Given a list of data items ordered by their expected access probabilities and a specification of the disk parameters, design an algorithm that assigns data items to disks and determines the interleaving of disks.
  The algorithm produces a periodic broadcast program with fixed inter-arrival times per data item.

## Slide 34: Broadcast disk program
An example:
Order pages from "hottest" to coldest (page is record of data with same format and length)
Partition pages into tracks ("disks") — pages in a track have similar access probabilities
Determine relative frequencies of the disks (e.g., rel_freq (1) = 3, rel_freq (2) = 2)
Split each disk into "chunks"
  maxchunks = LCM(relative frequencies)
  numchunks(J) = maxchunks / relativefreq(J)
Broadcast program is then:
  for I = 0 to maxchunks - 1
  for J = 1 to numdisks
  Broadcast( C(J, I mod numchunks(J) )

## Slide 35: Broadcast disk program
An example:
rel_freq (1) = 4
rel_freq (2) = 2
rel_freq (2) = 1

## Slide 36: Selective tuning
  Clients may actively listen to thousands of data records on the broadcast just to pick up one of them to use.
Selective tuning is the process by which MU selects only the required data records, tunes to them, and caches them
  MU activates only when the data arrives, saving power consumption
How to enable selective tuning?
  Place a structure and overhead over the broadcast data
  In addition to data, each broadcast cycle broadcasts a directory or index which is the overhead prefixed by server before the data
  A disadvantage of selective tuning is that it extends the broadcast cycle and hence increases taccess

## Slide 37: Selective tuning
An example:
n records R0 to Rn–1 interleaved and broadcast as in a multi-disk model
Only the records Ri' and Rj' are of interest and required by applications on a device
The broadcast disk broadcasts Ri ' and Rj ' thrice and once, respectively, as the subscription probability of Ri ' is three times that of Rj ‘
The record Ri' is partitioned into k buckets, bi0 to bik–1
The record Rj' is partitioned into k‘ buckets, bj0 to bj k'–1. Each bucket has equal length lb, which means equal number of bits and the devices takes identical time lb × ts to cache each bucket data. [ts the time interval between successive bits]
In addition to data, each broadcast cycle broadcasts a directory, or index which is the overhead prefixed by server before the data
Device selects only the buckets of Ri’ and Rj ' which are of interest and receives the signals only during first, second, or third instances of Ri ' or during instances of Rj' , that is, during the intervals Ti0,… ,Ti k–1, Tj0, … ,Tjk'–1 of broadcasting of bi0 … bi k–1, bj0 … bj k'–1, respectively
In the remaining intervals, where either the other records which are not of interest are being broadcast or when record of interest is already cached in an earlier broadcast cycle, the device remains idle.
During this period it does not dissipate power and hence saves energy

## Slide 38: Directory method
Broadcasting a directory as overhead at the beginning of each broadcast cycle
  A directory specifies when a specific record or data item appears in data being broadcasted, consisting of start sign, pointers to records, and end sign
  If interval between the start of the broadcast cycles is TB, then directory broadcasts at each successive intervals of TB
A device has to wait for directory before it can get tuned to its interested data and then start caching it
  Recall that tuning time ttune is the time taken by the device for selection of desirable records.

## Slide 39: Index-based method
Indexing is another method for selective tuning, used to guide the MU in the listening process
  Index can be broadcast interleavingly with data records.
  Index only contains key names so is relatively small.
  A traditional database index maps a key to where the key value is stored in memory; Here, an index for broadcast maps a key to the time when the key value is broadcast “on air”.
  When client is looking for information, it tunes to the channel to locate the index for the broadcast cycle – gets broadcast time of the data and sleep until it arrive.
inx
inx
inx
inx
inx
inx
inx
inx
inx
inx

## Slide 40: Index and offset
At each location (data record), an offset value may also be specified
  An index maps to the absolute location of from the beginning of a broadcast cycle, while an offset maps to the beginning of the next index
  Offset is used by the MU along with the present location to calculate the wait period for tuning to the next record

## Slide 41: (1, m) indexing
Broadcast the index every fraction 1/m of the broadcast data items.
  An index transmits m times during each period of the broadcast.
All data items have an offset to the beginning of the next indexed data item.
  To access a record, a client tunes into the current data item on the channel, uses the offset to tune in again when the index appears.
  From the index, it determines the required data item.

## Slide 42: (1, m) indexing
An algorithm is used to adapt a value of m such that it minimizes the access latency in a given wireless environment
  Index format is adapted to with a suitable m chosen as per the wireless environment, so as to decrease the probability of missing the index
  If m is chosen small then the power dissipated by device is less but the data access latency increases
  The value of m therefore needs to be optimized by employing an algorithm

## Slide 43: Distributed indexing
Improves over the (1, m) method
  instead of replicating the whole index (large overhead), each index segment describes only the offset of data items which immediately follow
Each index I is partitioned into two parts I' and I″
  I″ consists of unrepeated k levels (subindexes), which do not repeat and I′ consists of top j repeated levels (subindexes)